## Slide 1
PROGRAMMING LABORATORY-III
Embedded operating system

## Slide 2: Practical List
Assignment No | Problem Statement
A1 | Develop an application using Beaglebone Black/ARM Cortex A5 development board to simulate the operations of LIFT.
A2 | Develop an application using Beaglebone Black/ ARM Cortex A5 development board to simulate the working of signal lights
B1 | Write an application to and demonstrate the change in Beagleboard/ARM Cortex A5/Microprocessor/CPU frequency or square wave of Programmable frequency.
B8 | Develop a network based application by setting IP address on BeagleBoard/ARM Cortex A5
C1 | Develop Robotics(Stepper Motor)Application using Beagle Board.

## Slide 3: Course Objectives & Outcomes
Course Objectives:
  To learn Embedded Operating system programming
  To learn writing software engineering document
  To learn Embedded/Concurrent and distributed programming
Course Outcomes:
  Ability to perform embedded operating systems programming
  Ability to write software engineering document
  Ability to perform concurrent and distributed programming.

## Slide 4
was founded to give developers, hobbyists and students robust open-source hardware development platforms
so they could quickly and cost effectively assemble systems by leveraging the many advantages of the open-source ecosystem.
BeagleBoard, BeagleBoard-xM, BeagleBone and now BeagleBone Black provide flexible and expandable opensource platforms for all electronic artists

## Slide 5: Features of BBB
Based on the Sitara AM3358BZCZ100 ARM Cortex-A8 processor from TI
1GHz Linux Computer
4KB EEPROM
512MB of low-power DDR3L RAM
4GB 8-bit eMMC
microSD card slot: expandable up to 32GB
USB Host, Ethernet & HDMI interface
2 X 46 pin header
Debian OS

## Slide 6: Beagleboard

## Slide 8: KIT Description
DC Power is the main DC input that accepts 5V power.
Power Button alerts the processor to initiate the power down sequence.
10/100 Ethernet is the connection to the LAN.
Serial Debug is the serial debug port.
USB Client is a miniUSB connection to a PC that can also power the board.
BOOT switch can be used to force a boot from the SD card.

## Slide 9
There are four blue LED’S that can be used by the user.
Reset Button allows the user to reset the processor.
uSD slot is where a uSD card can be installed.
microHDMI connector is where the display is connected to.
USB Host can be connected different USB interfaces such as Wi-Fi, BT, Keyboard, etc.

## Slide 11: Connectivity Options

## Slide 12: Expansion Header
Enable cape hardware and includes
  65 digital I/O
  7 analog
  4 serial
  2 SPI
  2 I2C
  8 PWMs
  4 Timers
  And much more

## Slide 13: Typical Setup
Two Options:
  Tethered to a PC
  Standalone
Tethered to PC
  Host machine (e.g. Ubuntu)
  Target Board (e.g. BBB)
  Mini USB to USB Type A Cable (P4 port)
Standalone
  5VDC 1A Power Supply
  HDMI monitor
  Micro HDMI to HDMI Cable
  USB wireless K/B mouse combo

## Slide 14: Communication between BeagleBoard and host machine using Minicom
Objective: A successful communication between Linux and BeagleBoard using Minicom terminal.
  Installation of Minicom
  Connect to Beagle board
  Configure Minicom
  Run minicom as root and test

## Slide 15: Installation of Minicom
you need to install Minicom so you can communicate with Beagle Board. Minicom is a text-based modem control and terminal emulation program for Unix-like operating systems.
If you are using CentOS or Fedora then you can type following command to install minicom. You need to perform this installation as a root.
$ su
$ yum install minicom
If you are using Ubuntu as a guest Linux OS then you need to type following command.
$ sudo aptget install minicom

## Slide 16: Connect to Beagle board

## Slide 17: Configure Minicom
If you are using Minicom first time, you need to set up its configuration and save it as a default configuration.
So next time you can directly use default configuration and no need to set all parameters again.
To open Minicom configuration window write following command.
$ minicom -s

## Slide 18
You will get the screen as below.

## Slide 19
Serial Port setup: By using Up and Down arrow key you can select Serial port setup option and you can see the following screen.

## Slide 20: Selecting Serial Device:
If you already connected beagle board as shown in Snapshot 1, then you can find USB/Serial (Laptop/PC) port then you can find it using dmsg command. I am experimenting with my notebook so I need to find which USB port is connected to Beagle Board.

## Slide 21
Press A to change serial device to ttyUSB0.

## Slide 22
Then click on “Exit from Minicom” next.
select “Save Setup as dfl”

## Slide 23: Boot into BBB
After connection open terminal in Ubuntu
Switch to super user ($sudo su)
It may ask password…
Open minicom setup (minicom –s)
In serial port setting
  ‘A’ setting must be /dev/ttyACM0
  ‘G’ & ‘H’ (H/w & S/w flow Control) setting must be ‘NO’
Save setup as default & exit
Target will boot & will ask login&password
After login switch to super user ($ su)

## Slide 24: Programming steps with BBB
Create folder for your project
Create source file in the folder, use vim Text Editor create source file
Compile source file (use g++ compiler)
Execute output file
Verify output

## Slide 25: Programming Beaglebone Black
Connecting using Minicom
Type
$ minicom –s
device name – ttyACM0

## Slide 26: Programming Beaglebone Black (Python)

## Slide 27: Blinking LEDs through GPIO Pins

## Slide 28: Programming Beaglebone Black (Python) – Blinking LED
import Adafruit_BBIO.GPIO as GPIO
LEDTop=“P8_9”
LEDBottom=“P8_10”
GPIO.setup(LEDTop, GPIO.OUT)
GPIO.setup(LEDBottom, GPIO.OUT) from time import sleep
for I in range(0,5):
GPIO.output(LEDTop,GPIO.HIGH)
sleep(1)
GPIO.output(LEDTop,GPIO.LOW)
sleep(1)
GPIO.cleanup()

## Slide 29: Programming Beaglebone Black (Python) – Blinking LED
import Adafruit_BBIO.GPIO as GPIO import time GPIO.setup("P8_9", GPIO.OUT) while True: GPIO.output("P8_9", GPIO.HIGH) time.sleep(0.5) GPIO.output("P8_9", GPIO.LOW) time.sleep(0.5)

## Slide 31: Reference
element14 BeagleBone Black System Reference Manual, April 2014

## Slide 32
Thank you !